DUMP BODY - SPECIFICATIONS

Model PBL-300

Dump Body Features:

No Cross members

High lift tailgate

Full depth corner posts

Rigid double acting tailgate

Pockets for extension sideboards are standard

Strong tailgate chains furnished as standard

Easy acting tailgate control with positive acting lower hinge hook

All steel tailgate hardware

Provision for Fed 108 lights

Enclosed rear corner posts

Rugged construction

Air tailgate control

Cab shield

14/16 Cubic yard capacity

Dump Body Options:

Sliding doors in tailgate

Asphalt apron

Hitch plate and hitch

Tarp system

Hoist Features:

Factory-installed body props

Unique lever control grips with operation instructions

Body raise indicator light

Backup alarm

High pressure telescopic hoist

Standard Metal Gauges & Specifications:

Floor 1/4" AR400

Sides 43" high, 3/16" steel

Front 53" high, 3/16" steel

Tailgate long members 53" high, 3/16" steel

Includes:

Body with hinge

Hoist with mounting trunnion

Wire harness

Light kit

Hose kit

Hydraulic pump, valve and tank

High lift tailgate power unit

Operator manual and safety decals

Air controls