DUMP BODY - SPECIFICATIONS

Model PBL-400

Dump Body Features:

No Cross members

High lift tailgate

Full depth corner posts

Easy acting tailgate control with positive acting lower hinge hook

All steel tailgate hardware

Provision for Fed 108 lights

Rugged construction

Air tailgate control

Cab shield

Dump Body Options:

Sliding doors in tailgate

Asphalt apron

Hitch plate and hitch

Tarp system

Hoist Features:

Factory-installed body props

Unique lever control grips with operation instructions

Body raise indicator light

Backup alarm

High pressure telescopic hoist

Standard Metal Gauges & Specifications:

Floor 1/4" AR400 Steel

Sides 45" high, 1/4" AR400 Steel

Front 45" high, 1/4" AR400 Steel

Tailgate 45" high, 1/4" AR400 Steel

Includes:

Body with hinge

Hoist with mounting trunnion

Wire harness

Light kit

Hose kit

Hydraulic pump, valve and tank

High lift tailgate controls

Operator manual and safety decals

Air controls