TRAILER EMULSION SPRAYER - SPECIFICATIONS

Model 220-CT

These specifications describe a trailer mounted emulsion and cutback sprayer.

Tank:

Round Cross section, 200 gallon.

ASME Construction 125 PSI.

6" Fill Opening hinged.

2" Drain plug.

10 Gallon Waste Recovery Tank.

Y Strainer on discharge.

Basket Strainer in Fill Opening.

Safety Air Exhaust Valve.

Safety Pressure Valve.

Pressure Regulators & Gauges.

Air Blow Out for Cleaning.

Engine:

Four Cycle, 5 HP @ 3600 RPM.

Equipped with Throttle Control.

Centrifugal Clutch and Reduction.

Pump:

12 CFM Displacement.

2 Cylinder, Air Cooled, Single Stage.

Air Unloader.

LPG Heater:

4" Heat Tube full length of Tank.

LPG Fueled.

150,000 BTU Burner with outfire protector.

8-Gallon Fuel Tank with Regulator.

50°F - 500°F Thermometer.

Hand Spray:

25-ft 1/2 inch Hose.

5 ft Wand with Shut off Valve.

Trailer:

4" Channel Frame.

3,500 lb. Rated Capacity.

Springs 3,200 lb. Rated Capacity.

Tires 6.70 X 15 Rated Capacity.

Retractable Frame Jack.

Heavy Duty Fenders.

ICC Lighting.

Safety Chain.

2" Ball Hitch.

OPTIONAL EQUIPMENT:

Brakes - Electric or Hydraulic.

Pintle Hitch or Ball.

Electric Auxiliary Heater.

LPG Engine.

Lockage Engine & Cover.

Electric Start Engine.

6 ft. Spray Bar.

Hand Torch.

Spray Hose Reel.

Dual Spray Hose & Wand - Air/Material.

10-Gallon Solvent Tank.