EMULSION SPRAYER - SPECIFICATIONS

Model BH-205-28

Emulsion Spray Unit:

Emulsified Asphalt spray and storage system mounted on Truck chassis for applying tack coat.

Tank:

Two compartment tank.

Storage capacity 177 gallon emulsion and 28 gallon solvent.

10 gauge steel with the bottom reinforced.

6” curbside filler cap.

Tank dimension 72”W x 24”L x 30”H.

4” clean out on curb side near tank bottom.

Tank shall be vented.

Removable fill basket strainer.

Y strainer at the discharge of tank before material enters the pump.

Capable of switching from emulsion to solvent with one valve lever.

Heater:

Internal serpentines of 1” steel tubing to circulate water from truck engine.

Truck engine cooling system as a heat source.

Two 5/8 inch coolants hose.

System will have a temperature control valve at the tank.

Auxiliary Electric Heat:

Equipped with 110 VAC heat system.

Overnight heating controlled by temperature sensor.

Heating elements shall be low-density stainless steel.

Mounting:

Space required for mounting of tank is 30 inch.

Spraying system shall be mounted in front of dump body.

Mounting shall be accomplished with 2 full length mounts.

Spring bolsters on one side of tank.

Bolting to frame shall consist of 3 each side, 1/2 inch.

No welding on truck frames will be accepted.